BSD Router Project diagrams

---
Logical view
192.168.12.0/24
2001:db8:12::/64
Router 1
Router 2
192.168.20.0/24
2001:db8:20::/64
Loopback 2
192.168.13.0/24
2001:db8:13::/64
192.168.40.0/24
2001:db8:40::/64
loopback 4
192.168.34.0/24
2001:db8:34::/64
Router 4
Router 3
Admin vlan
Routed vlans
RIP and RIPng domain
EBGP domain
OSPF v2/v3 domain
10.0.0.0/24
TAP,vlan 0
Admin workstation (qemu host)

---
192.168.12.0/24
2001:db8:12::/64
Router 1
Router 2
192.168.20.0/24
2001:db8:20::/64
Loopback 2
192.168.13.0/24
2001:db8:13::/64
192.168.40.0/24
2001:db8:40::/64
loopback 1
RIP and RIPng domain
EBGP domain
OSPF v2/v3 domain
192.168.34.0/24
2001:db8:34::/64
Router 3
Router 4

---
192.168.12.0/24
2001:db8:12::/64
Router 1
Router 2
em0: .1
em0: .2
192.168.20.0/24
2001:db8:20::/64
Loopback 1
em1: .1
192.168.13.0/24
2001:db8:13::/64
192.168.40.0/24
2001:db8:40::/64
loopback 1
RIP and RIPng domain
EBGP domain
OSPF v2/v3 domain
em0: .3
192.168.34.0/24
2001:db8:34::/64
em2 : .4
em2 :.3
Router 3
Router 4

---
R1
em3: . 1
192.168.10.0/24
em3: . 2
em3: . 3
ucarp3: .254
R3
R2
ucarp4: .254
em4: . 2
em4: . 3
10.0.0.0/24
em4: . 4
R4

---
vtnet3: . 3
192.168.1.0/24
vtnet3: . 1
vtnet3: . 2
VRRP: .254
VRRP: .254
vtnet4: . 1
vtnet4: . 2
192.168.2.0/24
vtnet4: . 4

---
vtnet3: . 1
inside
192.168.10.0/24
vtnet3: . 2
master carp : .254
vtnet3: . 3
backup carp
vtnet1 : .2
vtnet1 : .3
pfsync : 192.168.23.0/30
outside
vtnet4: . 2
master carp : .254
vtnet4: . 3
backup carp
vtnet4: . 4
10.0.0.0/24

---
Carrier 1
Carrier 2
Bird routing table
default
Bird protocol
BGP 1
pipe
pipe
Bird protocol
BGP 2
Bird protocol
Kernel (default fib)
Bird routing table
Carrier 1
Bird routing table
Carrier 2
vtnet0
default fib
vtnet1
default fib
Bird protocol
Kernel (fib 1)
Bird protocol
Kernel (fib 1)
vtnet2
fib 1
vtnet4
fib 2
Bird protocol
Kernel (fib 2)
pipe
pipe
vtnet3
default fib
Bird routing table
member 2
Bird routing table
member 1
Bird protocol
OSPF 1
Bird protocol
OSPF 2
R5
R6
OSPF member 1
OSPF member 2
FullBGP member

---
Routing tables
Protocols
Default
Kernel
(FIB)
device
direct
Export filter
(default : none)
static
BFD
Import filter
(default : all)
BGP
Other
OSPF
RIP
pipe

---
10.0.1.0/24
2001:db8:1::/64
vtnet0: .1
R1 (OpenVPN client)
vtnet3: .1
192.168.15.0/24
2001:db8:15::/64
vtnet0: . 5
R5
vtnet1: .5
vtnet3: .4
vtnet2: .3
+200ms
latency
+100ms
latency
192.168.25.0/24
2001:db8:25::/64
192.168.45.0/24
2001:db8:45::/64
192.168.35.0/24
2001:db8:35::/64
vtnet3: .2
vtnet3: . 4
vtnet3: .3
(OpenVPN server)
(OpenVPN server)
(OpenVPN server)
vtnet4: .2
vtnet4: .4
vtnet4: .3
10.0.2.0/24
2001:db8:2::/64

---
R1 (client)
vtnet0: .1
10.0.12.0/24
2001:db8:12::/64
vtnet0: . 2
R2 (ECMP)
vtnet1: .2
vtnet2: .2
10.0.23.0/24
2001:db8:23::/64
10.0.24.0/24
2001:db8:24::/64
vtnet1: .3
vtnet1: . 4
vtnet3: .3
vtnet3: .4
10.0.35.0/24
2001:db8:35::/64
10.0.45.0/24
2001:db8:45::/64
vtnet3: .5
vtnet2: .5
R5 (ECMP)
vtnet4: .5
10.0.56.0/24
2001:db8:56::/64
vtnet4: .6
R6 (server)

---
R5
iperf server
Asymetric line
100M download
50M upload
To be fair shared by all active users
vtnet3: .5
10.0.5.0/24
2001:db8:5::/64
vtnet3: .4
DHCP server
Traffic shapping
10.0.0.0/24
2001:db8:0::/64
vtnet4: .4
vtnet4: . 3
vtnet4: .1
vtnet4: .2
User 1
User 2
User 3

---
R6
R5
(RR)
AS65535
AS64512
R7
TCP MD5
AS100
AS200
10.0.4.0/24
2001:db8:4::/64
R5
R6
(RR)
. 5
vtnet4
. 6
. 5
. 6
10.0.6.0/24
2001:db8:6::/64
10.0.3.0/24
2001:db8:3::/64
10.0.5.0/24
2001:db8:5::/64
.2
vtnet3
vtnet6
vtnet5
 . 1
. 3
. 4
. 7
10.0.2.0/24
2001:db8:2::/64
R7
. 3
vtnet2
. 4
vtnet0: . 1
vtnet0: . 1
10.0.1.0/24
2001:db8:1::/64
10.0.7.0/24
2001:db8:7::/64

---
10.0.23.0/24
88.88.88.0/24
em0
em1
em2
BAS (PPPoE server)
LAC (L2TP client)
LNS (L2TP server)
PPPoE client
Web server
PPPoE
L2TP
PPP

---
vr0 (fast ethernet)
vr0 (fast ethernet)
PC 2
HP Compaq T5000
Thin client
PC 1
HP Compaq T5000
Thin client

---
Switch (gigabit)
Netgear GS608 v3
vr0 (fast ethernet)
vr0 (fast ethernet)
PC 2
HP Compaq T5000
Thin client
PC 1
HP Compaq T5000
Thin client

---
Switch (gigabit)
Netgear GS608 v3
vr0 (fast ethernet)
10.0.1.1
vr0 (fast ethernet)
10.0.2.2
PC 2
HP Compaq T5000
Thin client
PC 1
HP Compaq T5000
Thin client
sis0 (fast ethernet)
10.0.1.254
sis1 (fast ethernet)
10.0.2.254
Router
PC engine WRAP 1e203

---
- DHCP Server
- Quagga
- ATLQ (shape VPN IPv4 to 64Kb/s)
loopback1
10.0.3.3/24
2001:db8:3::3/64
em1 (.3)
em2 (.3)
RIP
OSPF
- Bird
- mpd
- IPFW (shape VPN IPv6 to 128Kb/s)
- freevrrpd
- Quagga
- mpd
- netflow
em1 (.2)
em2 (.4)
2 PPTP VPN
(IPv4 and IPv6)
em0 (.2), carp (.254)
IPv4 DHCP relay
IPv6 rtavd
em3 (.4), VRRP (.254)
IPv4 DHCP relay
IPv6 rtavd
10.0.12.0/24
2001:db8:12::/64
10.0.45.0/24
2001:db8:45::/64
lagg0 (lacp:em0, DHCP client)
lagg0 (failover : em3, DHCP client)
R5
- Iperf server
- bsnmpd
- Iperf client
- Configs repo
em4 : .12
em4 : .14
em4 : .13
em4 : .15
em4 : .11
192.168.56.0/24
shared-with-host
10.0.34.0/24
2001:db8:34::/64
10.0.23.0/24
2001:db8:23::/64

---
- DHCP Server
- Quagga
- ATLQ (shape VPN IPv4 to 64Kb/s)
loopback1
10.0.3.3/24
2001:db8:3::3/64
em1 (.3)
em2 (.3)
iBGP
(TCP-MD5)
OSPF
- Bird
- mpd5
- IPFW (shape VPN IPv6 to 128Kb/s)
- freevrrpd
- Quagga
- mpd5
- netflow
em1 (.2)
em2 (.4)
2 PPTP VPN
(IPv4 and IPv6)
em0 (.2), carp (.254)
IPv4 DHCP relay
IPv6 rtavd
em3 (.4), VRRP (.254)
IPv4 DHCP relay
IPv6 rtavd
10.0.12.0/24
2001:db8:12::/64
10.0.45.0/24
2001:db8:45::/64
lagg0 (lacp:em0, DHCP client)
lagg0 (failover : em3, DHCP client)
R5
- Iperf server
- bsnmpd
- Iperf client
- Configs repo
em4 : .12
em4 : .14
em4 : .13
em4 : .15
em4 : .11
192.168.56.0/24
shared-with-host
10.0.34.0/24
2001:db8:34::/64
10.0.23.0/24
2001:db8:23::/64

---
R1 : DHCP Client
em0 : dynamic
10.0.12.0/24
em0: . 2
R2 : DHCP Relay
em1: . 2
10.0.23.0/24
em1 : .3
R3 : DHCP Server

---
One aggregated link
with a total 40Mb/s bandwitdh
Fast connected server
(more than 40Mb/s here)
Internet
ISP link 1
ISP link 2
ISP link 3
Multi ISP connected router
Aggregation server
Terminate tunnels and NAT
10Mb/s
10Mb/s
20Mb/s

---
vtnet3
.2
vtnet0
.2
lo1
10.6.6.6/32
lo1
10.1.1.1/32
vtnet0
 .1
vtnet1
.5
vtnet0
 .3
vnet 2
.5
vtnet1
.1
vtnet3
.3
.5
.6
R5
10.0.13.0/24
vtnet4
10.0.56.0/24
vtnet2
 .1
vtnet 3
.5
MLVPN client
R6
MLVPN Server
Aggregation server
vtnet3
 .4
vtnet0
 .4
10Mb/s
20Mb/s
10Mb/s
10.0.25.0/24
10.0.12.0/24
10.0.14.0/24
10.0.45.0/24

---
One aggregated link
with a total 20Mb/s bandwitdh
Fast connected server
(more than 20Mb/s here)
Internet
ISP link 1
ISP link 2
Multi ISP connected router
Aggregation server
Terminate tunnels and NAT
10Mb/s
10Mb/s

---
vtnet2
.2
vtnet0
.2
lo1
10.5.5.5/32
lo1
10.1.1.1/32
vtnet0
 .1
vtnet1
.4
vtnet0
 .3
.4
vtnet1
.1
.3
.4
.5
MLVPN client
10.0.13.0/24
vtnet3
10.0.45.0/24
vtnet2
10.0.34.0/24
R5
MLVPN Server
Aggregation server
10Mb/s
10Mb/s
10.0.24.0/24
10.0.12.0/24

---
Internet
.2
10.0.12.0/24
vtnet0 : .1
.3
vtnet1: .1
10.0.13.0/24
vtnet2 : .1
10.0.14.0/24
.4

---
ix0 : .1
1.1.1.0/24
2001:db8:1::/64
10Gb/s
ix0 : .2
L2TP/MLVPN client
igb0 : .2
One aggregated link
with a total 2Gb/s bandwitdh
igb3 : .2
10.1.23.0/24
1Gb/s
10.0.23.0/24
1Gb/s
igb3 : .3
igb2 : .3
L2TP/MLVPN server server
lo1
3.3.3.3/32
2001:db8:3::3/64

---
vtnet0
:1
vtnet0
:2
10.0.23.0/24
2001:db8:12::/64
NAT64
Default inet4 gw => R2
Default inet6 gw => R2
vtnet1 .2
vtnet1
.3

---
mcast source
PIM-DM
mcast receiver
PIM-DM
.1
.4
.2
.2
.3
.3
em0
10.0.12.0/24
em2
10.0.34.4/24
em1
10.0.23.0/24

---
cRP
cBSR
mcast source
PIM-SM
mcast receiver
PIM-SM
.1
.4
.2
.2
.3
.3
em0
10.0.12.0/24
em2
10.0.34.4/24
em1
10.0.23.0/24

---
Tunnel
10.0.24.0/24
2001:db8:24::/64
10.0.12.0/24
2001:db8:12 ::/64
10.0.45.0/24
2001:db8:45 ::/64
1.1.23.0/24
2001:db8:23 ::/64
1.1.34.0/24
2001:db8:34 ::/64
.2
.1
.2
.3
.3
.4
.5
.4
em0
em2
em3
R5
em1

---
em3
10.0.23.0/24
10.0.35.0/24
em2
10.0.12.0/24
10.0.56.0/24
R5
Multicast source
R6
Multicast client
10.0.45.0/24
10.0.24.0/24
em0
.1
em0
.2
em1
.2
em1
.3
em2
.2
em1
.4
em3
.4
em3
.5
em4
.5
em4
.6

---
BSDRP2
BSDRP3
em0
1.1.1.2/24
em0
1.1.1.3/24
bce1
bge1
Gi0/8
Gi0/6
Gi0/5
Gi0/9
cisco WS-C3550-12T